## Slide 1
reV Demo for RPM Clusters
Katy Waechter, Travis Williams

## Slide 2: The Renewable Energy Potential (V) Model
reV is a geospatial platform for assessing system performance, available capacity, distance to transmission, and total costs for potential solar and wind energy deployment at regional to continental scales.
Distance to Transmission
Available Capacity
System Performance & Costs
Notes: The reV model is a platform for assessing renewable energy potential and its geospatial intersection with grid infrastructure and land use characteristics.

## Slide 3: Answering Big Questions for Energy Planning
What are the land-use requirements and impacts of increasing levels of renewable energy deployment?
What are the transmission and integration costs of renewable energy deployment?
What are the impacts of inter-annual resource variability on renewable energy cost and performance?
Notes: Coupling methodologies for maintaining spatiotemporal characteristics of variable renewable energy in spatially course capacity expansion and nodal-based production cost models

## Slide 4: Integral Part of a Modeling Community

## Slide 5: Model Coupling
reV produces data for a diverse set of models, each with varying degrees of spatial and temporal requirements

## Slide 6: reV is Flexible in Scope and Scale

## Slide 7: reV Model Diagram
Capacity Expansion Models

## Slide 8: National Solar Radiation Database (NSRDB)
Temporal Range: 1998-2020
Temporal Interval: 5-minute for select ranges, 30-minute
Spatial Resolution: nominal 4 km
Spatial Extent: Western Hemisphere

## Slide 9: WIND Toolkit
Temporal Range: 2007-2014
Temporal Interval: 5-minute
Spatial Resolution: nominal 2 km
Spatial Extent: North America (land and offshore)

## Slide 10: Accessing NSRDB and WIND Toolkit
Equinor users can access NSRDB and WIND Toolkit resource data via:
NREL Developer API
  Requires sign up; rate limited
Data transfer via HSDS
Direct download from NREL Sharepoint

## Slide 11: Generation Potential
reV couples with the System Advisor Model (SAM) to estimate time series capacity factors at the resource data resolution (e.g., 5-min, hourly)
Chart: Wind Power Curves
Resource Data set
System Performance Modeling

## Slide 12: Calculating Site-Based LCOE
CC: Capital Cost ($)
FCR: Fixed Charge Rate
FOM: Fixed Operations and Maintenance ($-Annually)
MW: System Size
NCF: Net Capacity Factor
LCOE cents/kWh

## Slide 13: Technical Exclusions
Exclusions provide a means to model siting considerations and resulting supply impacts.
Exclusions typically represent sociopolitical, ecological, and technical constraints.

## Slide 14: Solar and Wind Potential
Wind and solar potential is often assessed in terms of geographic (or resource), technical, and economic potential. The results of this analysis characterize the developable quantity, quality, and cost of wind and solar resources that can be sorted to represent a supply curve.
PV and Wind potential
Wind potential only
PV potential only

## Slide 15: Potential to Power Plants
Each wind farm and PV plant quantifies:
  Multi-year mean capacity factor (%)
  LCOE ($/MWh)
  Interconnection costs ($/MWh)
  Available land (sq.km)
  Potential capacity (MW)
The technical potential analysis is evaluated at 90m spatial resolution, but aggregated up to discrete power plants for supply curve analysis
Discrete PV power plant
Discrete wind farm

## Slide 16: Each site has an associated capacity factor profile

## Slide 17: Aggregating for Supply Curve: Technical Potential
Annual Technical Potential=
Available area (km2) * Capacity Density (MW/km2) * Mean Net Capacity Factor * 8760 hours
PV Plant
Wind Plant
Typically 28-36 MW/km2 Fixed-Tilt PV
Typically 3-5 MW/km2 Wind Plant
Determined through geographic exclusions and aggregating to discrete power plants
System generation and performance determined using solar and wind weather data

## Slide 18: Wind Scenarios
Scenario | Wind Capacity
All Land | 23 TW
Open Access | 15 TW
Reference | 7.8 TW
Limited Access | 2.3 TW

## Slide 19: Solar Scenarios
Scenario | Solar Capacity
All Land | 248 TW
Open Access | 179 TW
Reference | 104 TW
Limited Access | 29 TW

## Slide 20: Resources
Operation and set up:
GitHub page: https://nrel.github.io/reV
Reference:
GitHub repository: https://github.com/NREL/reV
Tutorial (in development):
reV-tutorial: https://github.com/WilliamsTravis/reV-tutorial
  Will be merged into official reV repository in February
reVx.RPM tools:
GitHub page: https://nrel.github.io/reVX/_cli/reV-rpm.html
GitHub repository: https://github.com/NREL/reVX

## Slide 21: Set Up
Use a virtual environment to manage Python packages for reV
1. Create a new environment
2. Activate the new environment
3. Install reV from the NREL channel
4. Verify installation success
Notes: reV, built in Python, is a complex, extensible, and modular framework developed on NREL’s flagship high performance computer, Eagle.

## Slide 22: Compute Environment
reV can run in 3 environments:
Eagle
AWS
Local machine
  * reV-gen and reV-econ modules only

## Slide 23: reV Model

## Slide 24: RPM Clusters Model
Clusters
Cluster Profiles

## Slide 25: File Inputs
The following reV modules were used in creation of RPM clusters and cluster profiles for the NYISO analysis:
Generation
Collect
Batch
Each reV module has variable input files and associated requirements.
Notes: Not covering Econ, Supply-curve, Representative-profiles

## Slide 26: File Inputs -- Generation
The generation module batches SAM across millions of resource pixels, allowing for multiple system configurations.
Currently supports pvwatts7, windpower, csp SAM modules
Project points (.csv)
Configurations:
  config_gen.json : settings for generation module
  config_sam.json : SAM generator configurations for those referenced in project_points.csv/config
gen_gid | config | res_gid
Site index of generation file; not necessarily same as res_gid | Nominative value used in config_sam.json | Site index of resource file

## Slide 27: File Inputs -- Collect
For runs on in compute environments where computations are distributed across multiple nodes, node generation output files need to be collected into 1 generation file. Subset generation files are divided based on a range of site indices (correspond to project_points.csv).
Configurations:
  config_collect.json : settings for gathering subset generation files

## Slide 28: File Inputs -- Batch
In situations where you need to compute multiple runs for the same locations, batch module is used to streamline model runs to create input configuration files and execute runs based on those configuration files.
Configurations:
  config_batch.json : configuration for all runs to batch; can be manually set or programmatically set (not part of existing reV pipeline)
    May cross-reference other config files (config_gen.json, config_sam.json)

## Slide 29: File Inputs -- Clusters
Generation h5 file:
Technical exclusions h5 file:
Configurations:
  Count of clusters per each balancing area
  config_aggregation.json : configuration for aggregation to supply curve points; used to create a dictionary of what technical exclusion layers to exclude/include/weight

## Slide 30: reVX.RPM -- Clusters
reVX, the Renewable Energy Potential(V) Exchange Tool, provides a set of tools to extract data from reV model outputs and interface with RPM. Users can install reVX similarly to reV by following instructions on the reVX Github page (https://nrel.github.io/reVX/index.html).

## Slide 31: Running reV
reV is mostly commonly run in the command line interface (CLI), regardless of compute environment. Individual modules can be run by calling them as arguments with corresponding config file(s). However, it’s preferred to use full pipeline execution to document model runs.
Configuration:
  config_pipeline.json : configuration for all modules to be executed for a given run set
    Must cross-reference other config files (config_gen.json, config_sam.json, config_collect.json, config_aggregation.json, …)

## Slide 32: Examples of reV CLI Commands
(base) user@users-computer:~/rev_folder$ conda activate revenv
(revenv) user@users-computer:~/rev_folder$ reV-gen from-config –c config_gen.json
(revenv) user@users-computer:~/rev_folder$ reV-collect from-config –c config_collect.json
(revenv) user@users-computer:~/rev_folder$ reV –c config_batch.json batch --dry-run –monitor-background
(revenv) user@users-computer:~/rev_folder$ reV –c config_batch.json batch --monitor_background --logdir ./logs
(revenv) user@users-computer:~/rev_folder$ reV-pipeline from-config –c config_pipeline.json
(revenv) user@users-computer:~/rev_folder$ reV –c config_pipeline.json pipeline

## Slide 33: File Inputs -- Clusters
Generation h5 file: capacity factor profile dataset (n, 8760)
Technical exclusions h5 file: build list of reV-grid indices to exclude/include/weight in evaluation of developable areas
RPM meta table (.csv): mapping of project points to balancing area and count of desired RPM Clusters per balancing area (varies by technology)
Configurations:
  parameters.json: concatenates set up info for RPM Clusters and configuration for aggregation (from config_aggregation.json); used to create a dictionary of what technical exclusion layers to exclude/include/weight

## Slide 34: File Inputs – Cluster Profiles
Generation h5 file: capacity factor profile dataset (n, 8760)
Technical exclusions h5 file : build list of reV-grid indices to exclude/include/weight in evaluation of developable areas
Configurations:
  Clusters table (.csv)
  config_aggregation.json : configuration for aggregation to supply curve points; used to create a dictionary of what technical exclusion layers to exclude/include/weight

## Slide 35: Running RPM Clusters & Profiles
Scripts used to call reVX.RPM tools are available in NREL Sharepoint:
  run_cluster_all.sh : bash script to kick off clustering.py that utilizes reVX.RPM.ClsuterManager.run_cluseters()
  run_profiles_all.sh: bash script to kick off profile_export.py that utilizes reVX.RPMOutput.process_outputs()
Alternatives: https://github.com/NREL/reVX/tree/main/examples/rpm

## Slide 36: Running reV Locally with HSDS
Conda and PIP requirements
Conda is the easiest way to install reV and its corollary reX (Resource Extraction Tool). To access resource datasets, a package called “h5pyd” will need to be installed via pip (Python’s native package manager).
Use the “nrel” channel
reV and reX are called “nrel-rev” and “nrel-rex”
If issues arise with h5pyd, try installing before the NREL packages

## Slide 37: Running reV Locally with HSDS
H5PYD
Python API for the Highly Scalable Distributed Service (HSDS)
Allows off-site users to access NREL resource HDF5 files stored on Amazon Web Services
Sign up for an account and API key here: https://developer.nrel.gov/signup/
Will need to configure a file to store these credentials as keys in a file named “~/.hscfg”:
hs_endpoint = https://developer.nrel.gov/api/hsds
hs_username = <user_name>
hs_password = <optional>
hs_api_key = <api key>
Alternatively, use the “hsconfigure” command as shown in the next slide

## Slide 38: Running reV Locally with HSDS
(base) user@users-computer:~/rev_folder$ conda create -n revenv python=3.7
(base) user@users-computer:~/rev_folder$ conda activate revenv
(revenv) user@users-computer:~/rev_folder$ pip install h5pyd
(revenv) user@users-computer:~/rev_folder$ conda install nrel-rev -channel=nrel
(revenv) user@users-computer:~/rev_folder$ hsconfigure
Enter new values or accept defaults in brackets with Enter.
Server endpoint: https://developer.nrel.gov/api/hsds
Username [None]: <your username>
Password [None]: <a password>
API Key: <enter key>
Testing connection...
connection ok
Save changes? (Y/N)
Saving config file to: ~/.hscfg
Example Installation (Linux, conda pre-installed)

## Slide 39: Running reV Locally with HSDS
(revenv) user@users-computer:~/rev_folder$ hsinfo
server name: NREL prod HSDS server
server state: READY
endpoint: https://developer.nrel.gov/api/hsds
username: <your username>
password: <the password>
server version: 0.5
node count: 8
up: 5 hours 29 min 13 sec
h5pyd version: 0.7.1
Verify Access to AWS

## Slide 40: Running reV Locally with HSDS
Verify reV Installation
(revenv) user@users-computer:~/rev_folder$ reV --help
Usage: reV [OPTIONS] COMMAND [ARGS]...
reV command line interface.
Options:
-n, --name STR Job name. Default is "reV".
-c, --config_file PATH reV configuration file json for a single module.[required]
-v, --verbose Flag to turn on debug logging. Default is not verbose.
--help Show this message and exit.
...

## Slide 41: Running reV Locally with HSDS
Verify reV Installation
(revenv) user@users-computer:~/rev_folder$ reV --help
…
Commands:
batch Execute multiple steps in a reV analysis...
collect Collect files from a job run on multiple nodes.
econ Econ analysis (lcoe, single-owner, etc...).
generation Generation analysis (pv, csp, windpower,...
multi-year Run reV multi year using the config file.
offshore Offshore gen/econ aggregation with ORCA.
pipeline Execute multiple steps in a reV analysis...
qa-qc Run reV QA/QC using the config file.
rep-profiles Run reV representative profiles using the config...
supply-curve Run reV supply curve using the config file.
supply-curve-aggregation Run reV supply curve aggregation using the...

## Slide 42: Running reV Locally with HSDS
Use “hsls” CLI commands to browse AWS filesystem
(revenv) user@users-computer:~/rev_folder$ hsls /nrel/
nrel_admin folder 2017-08-20 15:46:58 /nrel/
nrel_admin folder 2019-10-01 08:08:23 /nrel/nsrdb
nrel_admin folder 2020-06-10 15:14:46 /nrel/us-wave
nrel_admin domain 2017-08-20 16:06:29 /nrel/wtk-us.h5
nrel_admin folder 2019-10-01 08:07:38 /nrel/wtk
5 items
(revenv) user@users-computer:~/rev_folder$ hsls /nrel/nsrdb/india/
nrel_admin folder 2020-05-27 10:21:44 /nrel/nsrdb/india/
nrel_admin domain 2020-07-24 10:23:47 /nrel/nsrdb/india/india_spectral_tmy.h5
nrel_admin domain 2020-07-24 10:24:32 /nrel/nsrdb/india/nsrdb_india_2000.h5
nrel_admin domain 2020-07-24 10:25:21 /nrel/nsrdb/india/nsrdb_india_2001.h5
nrel_admin domain 2020-07-24 10:26:09 /nrel/nsrdb/india/nsrdb_india_2002.h5
nrel_admin domain 2020-07-24 10:26:59 /nrel/nsrdb/india/nsrdb_india_2003.h5
...

## Slide 43: Running reV Locally with HSDS
Use “hsls” to browse AWS datasets
(revenv) user@users-computer:~/rev_folder$ hsls /nrel/nsrdb/india/nsrdb_india_2000.h5
/ Group
clearsky_dhi Dataset {8784, 102300}
clearsky_dni Dataset {8784, 102300}
clearsky_ghi Dataset {8784, 102300}
coordinates Dataset {102300, 2}
dew_point Dataset {8784, 102300}
dhi Dataset {8784, 102300}
dhi_perez Dataset {8784, 102300}
dni Dataset {8784, 102300}
dni_perez Dataset {8784, 102300}
fill_flag Dataset {8784, 102300}
ghi Dataset {8784, 102300}
ghi_perez Dataset {8784, 102300}
...

## Slide 44: Running reV Locally with HSDS
Tell reV what to run
import json
import os
# Find these parameters with the SAM SDKTool: https://sam.nrel.gov/software-development-kit-sdk.html
sam_config = {
"array_type": 2,
"azimuth": 180,
"dc_ac_ratio": 1.3,
"gcr": 0.4,
"inv_eff": 96,
"losses": 14.07566,
"module_type": 0,
"system_capacity": 20000,
"variable_operating_cost": 0
}
# Write as a json
config_path = os.path.expanduser(“~/rev_folder”)
with open(config_path, "w") as file:
file.write(json.dumps(sam_config, indent=4))

## Slide 45: Running reV Locally with HSDS
Tell reV where to run
from rex import Resource
# Any file with the target points will work
NSRDB_SAMPLE = "/nrel/nsrdb/india/nsrdb_india_2000.h5"
# Get the meta object and filter for a desired coordinate range
with Resource(NSRDB_SAMPLE, hsds=True) as file:
points = file.meta
points = points[(points[“latitude”] > 37) & (points[“longitude”] > 97) ]
# Here, ‘gid’ is the grid ID and ‘config’ will tell reV which SAM file to run
points.index.name = "gid"
points = points.reset_index()
points[“config”] = “default”
# Save this as a csv, it can be used to configure reV
points.to_csv(“/home/user/rev_folder/project_points.csv”, index=False)

## Slide 46: Running reV Locally with HSDS
Tell reV where to run
# For India, these will contain elevation and time zone information
print(points.head())
gid latitude longitude elevation timezone config
0 100 15.05 67.05 0.0 4.0 default
1 101 15.15 67.05 0.0 4.0 default
2 102 15.25 67.05 0.0 4.0 default
3 103 15.35 67.05 0.0 4.0 default
4 104 15.45 67.05 0.0 4.0 default
5 105 15.55 67.05 0.0 4.0 default
6 106 15.65 67.05 0.0 4.0 default
7 107 15.75 67.05 0.0 4.0 default
8 108 15.85 67.05 0.0 4.0 default
9 109 15.95 67.05 0.0 4.0 default
10 110 16.05 67.05 0.0 4.0 default

## Slide 47: Running reV Locally with HSDS
Tell reV where to run (alternate method)
import os
from reV.config.project_points import ProjectPoints
# This requires the resource and sam configuration files
NSRDB_SAMPLE = "/nrel/nsrdb/india/nsrdb_india_2000.h5"
SAM_SAMPLE = os.path.expanduser("~/rev_folder/sample_sam_config.json")
# Create a list of coordinate pairs
coords = [[15.05, 67.05],
[15.15, 67.05],
[15.25, 67.05]]
# Create a point object with this reV method
points = ProjectPoints.lat_lon_coords(coords, NSRDB_SAMPLE, SAM_SAMPLE)
print(points.df)
gid config latitude longitude
0 100 ~/rev_folder/sample_sam_config.json 15.05 67.05
1 101 ~/rev_folder/sample_sam_config.json 15.15 67.05
2 102 ~/rev_folder/sample_sam_config.json 15.25 67.05

## Slide 48: Running reV Locally with HSDS
Run reV
import os
from reV.generation.generation import Gen
# Collect the elements generated from the previous slides
NSRDB_SAMPLE = "/nrel/nsrdb/india/nsrdb_india_2000.h5"
SAM_SAMPLE = os.path.expanduser("~/rev_folder/sample_sam_config.json")
POINT_SAMPLE = os.path.expanduser("~/rev_folder/project_points.csv")
# Tell reV which SAM configuration to use for each “config” key in the project points
sam_files = {
"default": SAM_SAMPLE
}
# The points object may be a path to a csv or a ProjectPoints object (as in from the previous slide)
gen = Gen.reV_run(tech=”pvwattsv5”, points=POINT_SAMPLE, sam_files=sam_files,
res_file=NSRDB_SAMPLE, max_workers=1, fout=None,
output_request=(“cf_mean”, “cf_profile”)

## Slide 49: Running reV Locally with HSDS
reV Output
# Access outputs with the .out dictionary and the data set key
print(gen.out[“cf_profile”])
[[0. 0. 0. … 0. 0. 0. ]
[0.002 0. 0. … 0.002 0.009 0.004 ]
[0.611 0.603 0.601 … 0.24 0.672 0.67 ]
...
[0. 0. 0. … 0. 0. 0. ]
[0. 0. 0. … 0. 0. 0. ]
[0. 0. 0. … 0. 0. 0. ]]
# Profile outputs are 2D Time X Site arrays
print(gen.out[“cf_profile”].shape)
(8760, 100)
# Mean outputs are 1D arrays
print(gen.out[“cf_mean”].shape)
(100,)

## Slide 50: Example Area of Interest

## Slide 51: Resource Data Scale

## Slide 52: reV Grid and Resource Data Scale

## Slide 53: Applying Technical Exclusions

## Slide 54: Aggregating to Represent Power Plants

## Slide 55: Modeling Grid Interconnection

## Slide 56: Calculating Techno-Economic Potential

## Slide 57: Supply Curve

## Slide 58: Cost Assumptions
Regional spurline cost multipliers
Regional capital cost multipliers
*Currently sourced from ATB 2020

## Slide 59: LCOE / LCOT Calculations
Total System Cost ($/MWh) = LCOE + LCOT
Levelized Cost of Energy
Levelized Cost of Transmission

## Slide 60
PV Plant
Substation
Transmission Line
What is the cheapest point of interconnection?
Load Center

## Slide 61
Spurlines

## Slide 62
What is the cheapest option when there are many competing sites?

## Slide 63: Total Capacity by Scenario
Scenario | Wind Capacity | Solar Capacity
All Land | 23 TW | 248 TW
Open Access | 15 TW | 179 TW
Reference | 7.8 TW | 104 TW
Limited Access | 2.3 TW | 29 TW

## Slide 64
What is the cheapest option when there are many competing sites?

## Slide 65: Supply Curve
Cheapest Sites
Expensive Sites
Each site contributes to the supply curve, with cheapest Total LCOE sites being earlier in the supply curve and more expensive sites being later in the curve
example
example
example